## Slide 1: Умные Компрессоры Верное Решение Smart Compressors The Intelligent Solution
Игорь Шокин / ВолкмарПфеил
Москва; март 2011
Игорь Шокин / ВолкмарПфеил
Москва; март 2011
BITZER Kühlmaschinenbau GmbH
Игорь Шокин / Волкмар Пфеил
Москва; март 2011

## Slide 2: Умные Компрессоры – Верное Решение
Agenda / Оглавление
  History - История
  Current Status - Современное состояние техники
  Case Study – Примеры
  Summary – Резюме

## Slide 3: History История

## Slide 4: Умные Компрессоры – Верное Решение
History - История
  Simple open type compressors with separate electrical motor
  Designed in 1940
  Simple open type compressor combined with mechanical valves & controls in condensing units

## Slide 5: Умные Компрессоры – Верное Решение
History – История
  Introduction of semi hermetic compressors (BITZER: BHS series)
  Paralleling of compressor to centralize and improve system efficiency

## Slide 6: Умные Компрессоры – Верное Решение
History - История
  Introduction of semi hermetic compressors with capacity regulation
    BITZERs efficient blocked suction concept
  Together with paralleling of compressors a nearly step less control
    With modern systems and lowest possible head pressures maybe not sufficient in winter times

## Slide 7: Умные Компрессоры – Верное Решение
History - История
  Introduction of compressors with external inverter; operating with nominal or reduced frequency
  Issues:
    Correct selection of inverter and motor size
    Programming and service of inverter
    Full cost increase no increase in cooling capacity due to no super synchronous operation

## Slide 8: Current Status Современное состояние техники

## Slide 9: Умные Компрессоры – Верное Решение
  Background - Selection of compressors & refrigeration systems
    Driving forces in the past
      Mainly initial investment costs
      Reliability
    Driving forces at the present time
      Efficiency improvements driven by
        Rising energy costs
        Reduced carbon footprint
        “Green” image
        Competitive advantages
      Live cycle costs
      Reliability

## Slide 10: Умные Компрессоры – Верное Решение
  Background - Selection of compressors & refrigeration systems
    Most refrigeration systems are predominantly working at part load conditions – however:
    Cooling capacity must be calculated for max. load under extreme operating conditions
      Huge “over capacity” at part load or low condensing temps.
    Therefore, capacity modulation is essential in many applications
      Match of capacity with cooling demands
      Improvement of energy efficiency through
        Improved dynamic system behaviour
        Smaller average temperature difference in heat exchangers
        Reduction of operating/ starting cycles

## Slide 11: Умные Компрессоры – Верное Решение
  Background - Selection of compressors & refrigeration systems
    Particularly MT systems in supermarkets feature strong fluctuations in cooling load
      Seasonal temperature profile – strong capacity changes over SDT
      Strongly varying loads: day, night, weekend, shopping frequency, possible heat reclaim systems, etc
    Present systems are mainly designed with multiple compressors and
    ON / OFF capacity control
    Dependent on boundary conditions & control regimes strong variations of suction and discharge pressures are apparent
    Conclusive Requirements
    Intelligent system control in combination with intelligent compressor capacity modulation in particular important with
      Low load conditions and/ or low ambient temperatures

## Slide 12: Умные Компрессоры – Верное Решение
Big potential for condensing temperatures 20°C or below!
Notes: <number>

## Slide 13: Умные Компрессоры – Верное Решение
Inverter operation?
    On/off operation of 4 compressors in a conventional supermarket system without an inverter

## Slide 14: Умные Компрессоры – Верное Решение
Current Status
Requirements on compressor design for high COP and SEER
  BITZER developed short stroke OCTAGON piston compressors which are best suited for over synchronous speed
Reduced piston velocity
Better discharging process
Less throttling losses
Higher frequencies possible
Improved running smoothness
Long stroke design Short stroke design
Same displacement
Same compressor speed

## Slide 15: Умные Компрессоры – Верное Решение
Current Status
  Octagon piston compressors with integrated inverter
    Higher specific cooling capacity due to 87 Hz operation
    Motor and inverter ideally matched
      Highest motor / inverter efficiency
      Wide application range
    Fully EMC qualified (industrial application)
    Suction gas cooled inverter
      Preprogrammed
      Maintenance free

## Slide 16: Smart Compressors − The Intelligent Solution
0
20
40
60
80
100
0
10
20
30
40
50
60
70
80
87
230V motor
120
140
160
180
Compressor
Frequency [Hz]
Power required P
[%]
Compressor
Voltage [V]
4EC-4.2Y
(R404A; to=-10°C; tc=45°C)
Power network: 400V-3-50Hz
Max motor current: 18.5A
Required at
Motor voltage:
Motor current:
Motor power:
Motor torque :
Available
Motor power:
Motor torque :
25 Hz
115 V
15.1 A
2.9 kW
34.1 Nm
2.9 kW
34.1 Nm
50 Hz
230 V
15.1 A
5.2 kW
34.0 Nm
5.2 kW
34.0 Nm
60 Hz
276 V
15.1 A
6.3 kW
34.3 Nm
6.3 kW
34.3 Nm
X
X
X
0
50
100
150
200
300
350
400
230
87 Hz
400 V
15.1 A
9.4 kW
35.4 Nm
9.4 kW
35.4 Nm
X
Frequency Inverter-Winding Layout 230V-3-50Hz (BITZER VARISPEED)
Torque required M

## Slide 17: Case Study

## Slide 18: Умные Компрессоры – Верное Решение
Example – payback period
Assumptions
    Constant cooling load: 47 kW
    Condensing temperature range: tc= 25°C … 45°C
    Condenser selection: t= 10K
    Installation location: Moscow, Russia

## Slide 19: Умные Компрессоры – Верное Решение
Assumptions
    Max./ min. capacities at
      to=-8°C; toh=10K, toh useful=10K, tCu=10K, w/o subcooling
      using R404A
      4CC-9.F3Y at 87Hz
Rack models | Compressors | Capacity | Control method
4CC standard | 3x 4CC-9.2Y | max.47,4 kW min. 15,8 kW | stepped 33 – 66 – 100%
VSD | 1x 4TCS-12.2Y 1x 4CC-9.F3Y | max.47,0 kW min. 7,4 kW | infinite 15,8 … 100%

## Slide 20: Умные Компрессоры – Верное Решение
Results
    Compressor COP can only be reached if compressor capacity equals the system capacity

## Slide 21: Умные Компрессоры – Верное Решение
Payback
COP improvement: 18%
Amortization period: less than 1 year!
Additionally has to be taken in consideration:
- Comparison based on constant load
- Winter operation leads to an additional COP reduction (standard rack)
due to relatively bigger steps and the smaller regulation range

## Slide 22: Умные Компрессоры – Верное Решение
/ Case study
ECOSTAR Smart air- cooled condensing unit with frequency inverter and intelligent control
Notes: <number>

## Slide 23: Умные Компрессоры – Верное Решение
 Case study:
   Conventional scroll unit vs. ECOSTAR unit with VSD:
   3 x L2500 show cases
   Operating conditions: R404a, SST=-4°C, 6-8°C show case temperature

## Slide 24: Умные Компрессоры – Верное Решение
  Case study - existing running store in Bangkok/ Thailand
    Installation 1: conventional scroll unit
    Installation 2: recip unit with VSD (ECOSTAR) as parallel system
    Each system operated for 6 days
    Monitoring of the power consumption by digital power meter
    Comparison on medium temperature application

## Slide 25: Умные Компрессоры – Верное Решение
  Case study – test result

## Slide 26: Умные Компрессоры – Верное Решение
 | Day 1 (kWh) | Day 2 (kWh) | Day 3 (kWh) | Day 4 (kWh) | Day 5 (kWh) | Day 6 (kWh) | Total (kWh) | Average (kWh)
Scroll on/off unit Power consumption | 93.2 | 82.2 | 93.2 | 94.9 | 96.8 | 96.0 | 556.3 | 92.7
Ecostar unit Power consumption | 60.1 | 69.0 | 71.5 | 76.2 | 70.6 | 68.4 | 415.7 | 69.3
ECOSTAR unit = 25.2% less energy
  Case study – test result

## Slide 27: Умные Компрессоры – Верное Решение
Case study - Life Cycle Cost Savings:
In 7 years ~ U$ 11,500.00
  Assumptions:
    7 years life cycle of standard CDU
    No energy cost increase in 7 years
    Energy cost based on lowest rate of U$ 0.1 /kWh (High energy cost areas will have more savings)
    Based on to = -4 °C, low temperatures leads to more savings
    Testing in tropical country, no full advantage on fan speed controller (Under low ambient conditions - more savings)

## Slide 28: Summary – Резюме

## Slide 29: Умные Компрессоры – Верное Решение
  Main drivers for capacity modulation
    Energy savings and emission reductions (incl. legislations)
    Quality of chilled products and/ or cooling process
    Improved components‘ reliability
  Resulting priorities in compressor and system developments
    Capacity adaption to real demand, intelligent control regimes
      Efficiency optimization related to load profile
      Operation at lowest possible condensing temperatures
      Reduced power of auxiliary drives in part load
    Energy efficiency at full and part load is major target & requirement
Notes: <number>

## Slide 30: Help Safe the World >> Reduce Energy BITZER believes in Inverter technology
Спасибо за внимание!
Спасибо за внимание!
Спасибо за внимание!